## Slide 1: GPU Architecture meeting 2

## Slide 2: Additional Hardware
As promised last time
Decoder
  Changes N width input into 2N width, with single bit enabled
  Useful for selecting one of 2N from N bits

## Slide 3: Additional Hardware
Hugely important!!!!
D- FlipFlop
  Holds onto input for whole clock cycle
  Takes new input @ (positive or negative) clock edge
  Enables a lot of computing

## Slide 4: Today’s Goals
Learn all about the next pieces of our processor
Instructions and Instruction Cycle
  What/why
  Instruction set
Registers
ALU

## Slide 5: Exercise
What does this number mean?
10001011000000100000000001000001

## Slide 6: Binary Refresher
0 and 1 only, pay attention to places
1101
To understand what number this is, we can take a sum of 2x, where x is the place of the number

## Slide 7: Binary Refresher
0 and 1 only, pay attention to places
We have a 1 in the zero’s, two’s, and three’s places
  So we can sum this as (1)20 + (0)21 + (1)22 + (1)23
    1 + 0 + 4 + 8 = 13
Place | 3 | 2 | 1 | 0
Value | 1 | 1 | 0 | 1

## Slide 8: Binary Refresher
What about negative numbers?
Sign Magnitude
  Most Significant Bit denotes sign
  Rest denotes magnitude
Two’s Complement
  Read the same, but different process
  Flip all bits, add 1
  This is how most computers do it because it makes subtraction (more on this later)

## Slide 9: Binary Refresher
So 1101 can be
Read as is: 1101 = 13
Sign Magnitude: 1101 = - (22+20) = -5
Two’s Complement: 1101 = - (0010 + 1) = - (0011) = -3
For our purposes, use online converters if necessary

## Slide 10: Exercise (cont.)
Maybe we know what this is now?
10001011000000100000000001000001
Maybe it’s negative?
  SM: -184680513
  2’s comp: -1962803135
Or maybe this isn’t just a really big number

## Slide 11: Assembly Languages
Processor’s toolbox
Near 1:1 with machine code
  Still kind of human readable
Designed and licensed out for processor dev
  Intel’s x86, ARMv8
  AMD RDNA and NVIDIA PTX for GPUs
Instruction Set Architecture
  Every Instruction the processor can do

## Slide 12: Assembly Languages cont.
Basics
Opcode – binary designated as a instruction type, bit width varies
  ADD, SUB, for example
Rd, Rm, Rn – Register operands
  Rd is the destination
  Rn and Rm are sources (nth, mth)
When written, registers denoted as X(number of register)

## Slide 13: Exercise (cont.)
So maybe this is assembly?
10001011000000100000000001000001

## Slide 14: Exercise (cont.)
So maybe this is assembly? (ARM)
[10001011000][00010][000000][00010][00001]
[ Opcode][ Rm][ Shamt][ Rn][ Rd]
[ ADD][ ][ ][ ][ ]

## Slide 15: Exercise (cont.)
So maybe this is assembly? (ARM)
[10001011000][00010][000000][00010][00001]
[ Opcode][ Rm][ Shamt][ Rn][ Rd]
[ ADD][ X2][ 0][ X2][ X1]
This is written in ARM as:
ADD X1, X2, X2 {ADD X1, X2, X2

## Slide 16: Expanding on the Instruction Cycle
Parts of a task that a computer needs to complete
Instruction Fetch
Register / Decode
Execute
Memory access
Write back

## Slide 17: Instruction Fetch
All instructions are kept in what’s called instruction memory
Essentially a queue of instructions to be completed
Pull a new one every clock cycle
Length of instruction depends on design

## Slide 18: Registers/Decode
Given an instruction from ifetch
Continuously hold data across clock cycles
From 2N registers, output the data from one
Be able to single out a register out of 2N to write to from N bits

## Slide 19: Execute
Given two data inputs of [ ] length + the instruction
Correctly compute addition, subtraction, and logical operations
Raise flags given correct circumstance
Select output based on encoded instruction

## Slide 20: Team split
All together | 
Decide ISA (instruction dimension impacts every other decision) | 
Register | ALU
Make Registers that hold data Make Mux that selects and outputs data from register Make decoder that selects a register to write | Make logic necessary for arithmetic (adder), and any desired logic Make mux that chooses output